## Slide 1: Firewalls
Network Security

## Slide 2: Firewall 553

## Slide 3: Firewalls - 553
Enforce network policy.
Usually firewalls are put on the perimeter of a network and allow or deny traffic based on company or network policy.
MUST have IP forwarding turned off*
Firewalls are often used to create a DMZ.
Generally are dual/multi homed*
Types of firewalls
  Packet filtering
  State full
  Proxy
  Dynamic packet filtering

## Slide 4: Packet filter - 555
Uses Access control lists (ACLs), which are rules that a firewall applies to each packet it receives.
Not state full, just looks at the network and transport layer packets (IP addresses, ports, and “flags”)
  Do not look into the application, cannot block viri etc.
  Generally do not support anything advanced or custom

## Slide 5: Packet Filter
Packet filters keep no state*
  Each packet is evaluated own it’s own without regard to previous traffic
  Advantages
  Disadvantages
    fragments
Rule based access control
Packet filters are still used on the edge of the network before a statefull firewall for performance reasons.

## Slide 6: State full firewall - 556
router keeps track of a connections in a table. It knows which conversations are active, who is involved etc.
It allows return traffic to come back where a packet filter would have to have a specific rule to define returned traffic
More complex, and can launch DoS against by trying to fill up all the entries in the state tables/use up memory.
If rebooted can disrupt conversation that had been occurring.
Context dependant access control*

## Slide 7: Proxy firewalls - 557
Two types of proxies
  Circuit level*
  Application*
Both types of Proxies hide the internal hosts/addressing from the outside world.
Talk about each of these on next slides

## Slide 8: Circuit Level Proxy - 559
A middleman.
A proxy takes client information and sends it to a remote server, it also receives a response and sends it back to the client.

## Slide 9: Circuit Level Proxies - 559
Main purpose is to hide internal network and stop direct communications between external machines and internal machines.
Advantages
Fairly simple
Works with all network protocols
Hides internal network addresses
When used with a firewall, stops people from directly starting conversations with internal hosts, while still allowing internal hosts to communicate with the Internet
Disadvantages
A single point of failure and performance issues
Does not analyze data does not protect from dangerous data
Cannot protect against, violations in the protocol or bad data being passed around,

## Slide 10: Application Proxies - 559
Like circuit layer proxies, but actually understand the application/protocol they are proxing.
This allows for additional security as they can inspect the data for protocol violations or content.

## Slide 11: Application Proxies - 559
Advantages
  Application proxies understand the protocol, so they can add extra security
  Can have advanced logging/auditing and access control features
    Ex. Restrict users to only allowed websites
    Ex. Inspect data for protocol violations
    Ex. Inspect data for malware (viri etc)
Disadvantages
  Extra processing requires extra CPU (slower)
  Proxies ONLY understand the protocols they were written to understand. So you generally have a separate application proxy for EACH protocol you want to proxy

## Slide 12: Application Proxies - 559
Examples:
  Squid web proxy server
  Internet Security and Acceleration Server (MS web proxy)
  SMTP proxies
  FTP proxies

## Slide 13: NAT/PNAT
A proxy that works without special software and is transparent to the end users.
Remaps IP addresses, allowing you to use private addresses internally and map them to public IP addresses
NAT allows a one-to-one mapping of IP addresses
PAT allows multiple private address to share one public address

## Slide 14: NAT

## Slide 15: PNAT

## Slide 16: NAT/PAT difference
NAT ONLY looks and rewrite the IP addresses*.
NAT requires 1 public IP for each computer that wants to access the Internet simultaneously. If you have 100 computer and you expect 20 of them to access the Internet at any time, 20 public IP addresses are required.
PAT looks at the IP and transport layer port number and rewrites both*
PAT only requires 1 public IP address and can support about 65,000 simultaneous connections for each IP public IP address.

## Slide 17: NAT / PNAT
Advantages
  Allows you to use private addresses Internally, you don’t need to get real public IP addresses for each computer
  Protects the network by stopping external entities from starting conversations to internal machines
  Hides internal network structure
  Transparent, doesn’t require special software
Disadvantages
  Single Point of Failure / Performance Bottleneck
  Doesn’t protect from bad content

## Slide 18: Overall Firewall best practices (563)
Block un-necessary ICMP packets types.
  (Be careful though, know your environment)
Keep ACLS simple
Use Implicit deny*
Disallow source routed packets*
Use least privilege*
Block directed IP broadcasts
Perform ingress and egress filtering*
Enable logging
Drop fragments or re-assemble fragments

## Slide 19: Overall Firewall issues
Potential bottleneck
Can restrict valid access
Often mis-configured
Except for application proxies firewalls generally do not filter out malware or improper content.
Don’t protect against internal attacks!*

## Slide 20: Firewall Architecture

## Slide 21: Security Zones
It is common practice in network and physical security to group different security levels into different areas or zones. Each zone is either more or less trusted then the other zones. Interfaces between zones have some type of access control to restrict movement between zones (like biometric and guard stations) or firewalls.) In Network security there is often a median zone between the Internet and internal network called a DMZ.

## Slide 22: DMZ
A buffer zone between an unprotected network and a protected network that allows for the monitoring and regulation of traffic between the two.
  Internet accessible servers (bastion hosts) are placed in a DMZ between the Internet and Internal network

## Slide 23: DMZ

## Slide 24: DMZ architectures
Multi-homed Firewall
Screened Subnet

## Slide 25: Multi Homed Firewall - 565
Multi-homed firewalls may be used to setup a DMZ with a single firewall. (see next slide)
On any multi-homed machine, IP forwarding should be disabled.*

## Slide 26: Multi-homed firewall

## Slide 27: Screened Subnet - 566
In a screen subnet, there is a separate firewall on both sides of the DMZ.
When using this model it is recommended that each firewall be a different vendor/product.
  Diversity of defense*

## Slide 28: Screened Subnet

## Slide 29: Multiple interface firewalls - 560
A firewall can be placed internally to protect internal networks from each other!

## Slide 30: Other Random Network Terms

## Slide 31: Other Technological security concepts (572)
Honey pot – a machine left open for attackers to attack.
Honey net – an entire network left open for attackers to attack.
Know the difference between entrapment and enticement?*

## Slide 32: NOS (568)
NOS - Network Operating System. All modern OSes are NOS.
  This just means they manage more than just the local computer, they usually provide or use network services in a client server architecture.

## Slide 33: DNS - 574
Network software uses IP addresses, however these are difficult for users to remember (especially in IPv6). So DNS is used to help map names that we use such as www.paladingrp.com to addresses that computers use like 63.251.179.13

## Slide 34: DNS
Common top level domains are
  .COM
  .EDU
  .MIL
  .GOV
  .ORG
  .NET
You should be aware of these above

## Slide 35: DNS cache poisoning - 577
Besides authoritative name servers organizations also have caching name servers that simply do DNS resolution on behalf of clients.
One common attack is DNS cache poisoning*

## Slide 36: DNS SEC
DNS sec tries to ensure integrity of DNS queries by digitally signing responses.* This attempts to defeat cache poisoning.